## Slide 1: Touch 22
Multi-touch Screen
And Painting Canvas
Logan Moseley, Dan Moseley, Danielle Geffert, Jon Wu

## Slide 2: The Touch Screen
Made with easily obtainable materials: plexiglass, LEDs, electrical wire, transistors, aluminum, and a webcam.
How it works:
  Infrared LEDs’ light bounces through the glass.
  When the surface is touched, some of the IR light is redirected to the webcam.
  The computer interprets the webcam vision into touches. Very sophisticated and very cool.
Notes: Logan

## Slide 3: Dan is testing out the screen. The camera is just two feet away, watching, waiting.3

## Slide 4: “uTouch” Painting Program
Very simple painting program.
Features are activated and deactivated by touching the button on the screen.
These features include color select, brush size select, lines, color fill, color sampling, clear\erase\undo, save\load, and shape stamps, as well as basic painting.
Like finger painting!
  Download uTouch.2
Notes: Danielle

## Slide 5
Touch 22’s uTouch
painting program in action.

## Slide 6: Why Multi-Touch?
Multi touch allows for multiple points of interaction with the screen.
It provides the ability to support multiple users simultaneously.
Touch-based computer interfaces are more intuitive, flexible, and fun than standard keyboard and mouse.
Notes: Jon

## Slide 7: Jon and Dan try to draw a stick figure. It’s not working out so well.3

## Slide 8: Construction
Cut aluminum to a frame for the glass.
Attach IR LEDs to the frame, connect LEDs to a battery via electric wiring.
Point visible light-filtered webcam at the glass.
TouchLib vision and calibration tools allow uTouch to “see” touches to the screen.
  See NUI Group for more details.1
Notes: Dan

## Slide 10: Development Software
TouchLib
  www.touchlib.com
TuioSimulator
  http://reactable.iua.upf.edu/?software
Adobe Flash Creative Suite 3
  http://www.adobe.com/products/flash/
Notes: Dan

## Slide 11: References
NUI Group TouchLib Forums
  http://nuigroup.com/forums/viewforum/27/
Google Code
  http://code.google.com/p/touch-22/
Touch 22 WikiDot
  http://touch22.wikidot.com/
Log Moseley, Dano Moseley, Ganielle Deffert, Jonny Wu
Notes: Logan